## Slide 1
PhytoSense
An Acoustic and Environmental Sensor Mesh Network
University of Oulu Botanical Garden
Romeo & Julia Greenhouses | May 2026
Plants make sounds when stressed. 1,200 exotic species. Nobody has listened yet.

## Slide 2
The Scientific Foundation
Khait et al., Cell 2023
Plants emit ultrasonic clicks (20-100 kHz) when stressed by drought or injury. Detectable up to 5 metres away.
2024: Maize disease detection
Acoustic IoT sensors detected northern leaf blight 4-5 days before visual symptoms appeared.
2025: Real-world conditions
Emissions stay detectable in noisy environments including wind, rain, and visitor activity.
What the field does not have yet: acoustic data from a diverse mixed-species greenhouse. Romeo & Julia hold 1,200 species from 4 climate zones.

## Slide 3
What Is PhytoSense?
A wireless sensor mesh network installed across Romeo and Julia.
Each node carries three sensors:
1
Ultrasonic microphone
Captures plant stress clicks in the 20-100 kHz range
2
Soil moisture probe
Flags zones that are too dry or overwatered
3
Humidity + temperature
Detects fungal risk conditions before damage appears
System Layers
Sensor Nodes (x4)
ESP32 + mic + soil + humidity
Gateway Node
Clock sync, localisation, MQTT
Raspberry Pi Hub
Dashboard, alerts, Excel logger

## Slide 4
Two Layers of Value
Scientific
First-of-its-kind research contribution
First systematic acoustic survey across 1,200 exotic species
Correlate acoustic events with the garden's accession database
Dataset cross-referenced with soil moisture and humidity
Methodology replicable by other botanical gardens worldwide
Direct pathway to 3 publication opportunities
Practical
Works from day one for garden staff
24/7 zone-level humidity, temperature, and soil moisture monitoring
Instant alerts when conditions drift outside safe thresholds
Visitor impact data across opening hours
Battery status and node health panel for staff
Live dashboard display for visitors as an interactive exhibit
vs

## Slide 5
Why Romeo & Julia?
One of the northernmost scientific gardens in the world. Two pyramid greenhouses. 1,200 exotic species from 4 climate zones.
Romeo
Tropical & Subtropical
Orchids
Carnivorous plants
Lianas & aquatic plants
Tropical fruits
Julia
Mediterranean, Desert & Temperate
Olives & vines (Vitis vinifera)
Geraniums & araucaria
Desert succulents
Temperate woodland
No laboratory in the world has access to this species diversity under one roof.

## Slide 6
Publication Opportunities
1
Species Acoustic Survey
Target journals:
Plant Signaling & Behavior
Frontiers in Plant Science
Sensors
A dataset of acoustic emission profiles across tropical, Mediterranean, and desert species in a real greenhouse. Fills a direct gap in the phytoacoustics literature.
2
Methodology Paper
Target journals:
HardwareX
Methods in Ecology & Evolution
A standardised open-source protocol for deploying low-cost acoustic mesh networks in mixed-species botanical collections. Replicable by any botanical garden.
3
Environmental Monitoring Study
Target journals:
Biosystems Engineering
Computers & Electronics in Agriculture
Microclimate heterogeneity across Romeo and Julia over a full seasonal cycle, including the impact of Finnish winter and daily visitor traffic on plant zones.

## Slide 7
MVP Cost
~EUR 218
total hardware cost
Component | Cost
ESP32 microcontrollers (x5) | ~EUR 40
Ultrasonic MEMS microphones (x4) | ~EUR 24
Soil moisture sensors (x8) | ~EUR 12
SHT31-D humidity + temp sensors (x4) | ~EUR 18
Raspberry Pi 4 (2GB) | ~EUR 55
Batteries, enclosures, cables, misc. | ~EUR 69
All software, firmware, and dashboards: EUR 0 (100% open source)
The dataset this generates cannot be replicated in a lab at any price.
No cloud services required.
Self-contained on local network.
Scales to 20 nodes without redesign.
Less than most research equipment purchases. More scientific output than most 3-year lab studies.

## Slide 8
Phased Roadmap
The committee is asked to fund Phase 1 only.
Phase 1
MVP
4 nodes
One zone, one greenhouse
Baseline dataset
First acoustic survey
Staff alerting live
This proposal
→
Phase 2
Full Romeo
10-12 nodes
All of Romeo greenhouse
Tropical species coverage
TDOA localisation
First publication
Future funding
→
Phase 3
Both Greenhouses
16-20 nodes
Romeo and Julia
Full research platform
Solar-powered nodes
Visitor dashboard
Future funding

## Slide 9
PhytoSense
The botanical garden is not a constraint
on this project. It is the reason the
project is scientifically interesting.
1,200
exotic species
EUR 218
hardware cost
3
publication paths
0
EUR software cost
University of Oulu Botanical Garden | Romeo & Julia | May 2026